1.	The instrumentation amplifier is shown below:

A)	Answer:

The INA’s non-inverting gain = (1+R4/R3) and its inverting gain = -(1+R2/R1)(R4/R3)

In a differential amplifier these gains must be equal => R1/R2 = R4/R3

If this condition is satisfied then the differential gain = (1+ R4/R3).

If the INA has a gain of 100 then R4/R3 = 99 = R1/R2 => R1 = R4 = 990k

B)	Answer:

Input offset voltage:            Vos = 1mV

Input offset current:            Ios  = 100nA

Input bias current:              Ib    = 50nA

Worst case contribution of offset: 1mV + 1mV = 2mV

Worst case contribution of input offset current = 2*100nA*10k  = 2mV

Worst case contribution of input bias current ~ 0 since 10K ~ 10k||990k

=> Detection limit = 4mV

C)	The maximum output swing is from 0 to 5V with a positive input signal, the output amplifier will clip immediately when a negative differential signal is applied. So the maximum differential input signal = 5/100 = 50mV.

D)	Vo = V1(1+R4/R3) – V2((1+R2/R1)(R4/R3)

Let the ratio R4/R3 = X and the ratio R1/R2 = X(1+d), where d is a fractional error

Vo = V1(1+X) – V2(1+1/X(1+d))*X = V1(X +1) – V2(X+1/(1+d))

Sanity Check: if d =0 => Vo = V1(X+1) – V2(X+1)

To find the differential and common-mode gains we can substitute 
V1 = Vcm + Vd/2 and V2 = Vcm –Vd/2

Vo = Vcm(X+1 - X+1/(1+d))  + Vd/2(X + 1 + X + 1/(1+d))

= Vcm(1- 1/(1+d)) + Vd/2(2X +1 + 1/(1+d))

Then CMRR = (2X + 1 + 1/(1+d))/ 2(1- 1/(1+d)) ~ (X + 1)/d

In the worst-case, we could have an equal and opposite error in the ratio R4/R3

So worst-case CMRR ~ 101/2*0.01 ~ 5000 => not bad

Another approach:

If Vo = V1*Aplus – V2*Amin

Then substituting V1 = Vcm + Vd/2 and V2 = Vcm –Vd/2 yields

Vo = Vcm* (Aplus-Amin) + Vd(Aplus + Amin)/2

So the CMRR = (Aplus + Amin)/2(Aplus-Amin)

2.	The following circuit employs two BJTs and four current sources to generate a voltage Vtemp that is proportional to absolute temperature.

A)	Answer:

Vtemp = VBE(3I) – VBE(I) = (kT/q)ln(3)

B)	The worst case situation is when the error is in the “I” branch.

Then Vtemp_err = (kT/q)[ln(3/1.01) - ln(3)]  OR  (kT/q)[ln(3/0.99) - ln(3)].

The sensitivity S of Vtemp = dVtemp/dT = (k/q)ln(3)

=> temp error = -T*ln(1.01)/ln(3) = +/-0.0091*(273.15 +21) =  +/- 2.7K

C)	At least 8 switches are required to allow each current source to be connected to the left or right BJT.

D)	There are 4 cases, of which three are the same:
Case 1: Vtemp = (kT/q)ln(3/0.99), 
Case 2,3,4: Vtemp = (kT/q)ln(2.99)

Then Vtemp_avg = (kT/q)[ln(3/0.99) + 3*ln(2.99)]/4 
Temp error =  (273.15 +21)[[ln(3/0.99) + 3*ln(2.99)]/4/ln(3)  –1] = 2.3mK

3.	 Figure below shows a fully differential amplifier based on a differential opamp with an input referred noise of 30 nV/√Hz.

A)	Input resistance = 200k => R1A = R1B = 100k. Gain of 100 => R2A = R2B = 10M

B)	Since the opamp introduces 30nV/sqrt(Hz)*(101/100) => the input resistors together contribute 40nV/sqrt(Hz). The noise of the output resistors is negligible because it appears at the output => divided by a gain of 100. A 1k resistor contributes 4nV/sqrt(Hz), so 40nV/sqrt(Hz) corresponds to a total resistance of 100k => each resistor is 50k (max).

C)	The input-referred ripple has an amplitude of 10mV*101/100 ~ 10mV

D)	The amplifier’s output-referred noise is 100*50nv/sqrt(Hz) = 5µV/sqrt(Hz).

After the filter, the rms noise = 5µV*sqrt[(1/2pRC)*(p/2)] = 5µV/sqrt(4RC).

We expect the ripple to be severely attenuated, so the ripple current through the resistor will be VIN,LPF/R. This current will charge a capacitor for half a clock period and cause a voltage change dV = VIN,LPF*T/2RC. The amplitude of the resulting triangular wave is half of this voltage change = VIN,LPF*T/4RC = 10mV*101*100µs/4RC => input-referred amplitude ~ 10mV*100µs/4RC

Equating the rms noise and the amplitude

=> 10mV*100µs/4RC = 5µV/sqrt(4RC) 
=> 1/5 = sqrt(4RC) => RC = 0.01 => fc = 1/2pRC = 15.9Hz

Check: amplitude of the triangular wave = 0.5*10mV*50us/0.01s = 25uV which is indeed quite small compared to 10mV.

4.	The thermistor readout system is shown below:

A)	In one clock cycle, C2 is charged up and then this charge is discharged to ground. So the total amount of charge transferred to ground Q = CVref.

This means that the average current Iref = dQ/dT = CVref*fVCO 
=> Rref = Vref/Iref =1/(fVCOC)

When the bridge is balanced, Rref = Rtherm = 6.6k => fVCO = 1/(6.6k*4pF) = 37.8MHz

As the temperature changes by 1mK then Rtherm = Rref will change by 0.3%/1000 
=> fVCO will change by 0.003*37.8kHz= 113.63Hz 
=> 0.3%/1000 => 1/ 333,333 => 19.34 bits resolution => 20 bits to be safe.

This is of course with respect to the nominal value of 37.8MHz.

B)	Opamp offset will cause the bridge to become slightly unbalanced. For a quarter bridge, we know that dV = Vdd*dR/R/4 => dV = 1.8*0.0003/4 = 0.135mV

D)	A non-linear VCO transfer function has no effect on the circuit’s performance because of the opamp’s infinite gain. VCO jitter, however, will look like extra thermal noise. Charge injection of both switches will cause errors in the net charge drawn from C1 and hence in the effective value of Rref.5. Consider the auto-zeroed amplifier shown below:

A)	When the amplifier is in unity-gain its output voltage = Vos => there is a small error voltage across its input = Vos/(A+1). If Vos/(A+1) < 1uV => A > 10,000.

B)	In the auto-zeroing phase the settling is limited by one R and the two capacitors in series, while in the amplification phase the settling is limited by 2R and two capacitors in series. So the worst-case settling time constant occurs during the amplification phase and is equal to RC.

 Exponential settling implies Verr = Vin*exp(-t/RC) => 13.5*RC < 10us 
=> C < 372pF

C)	In the auto-zeroing phase, the opamp is in unity-gain. Its bandwidth may then limit the settling. In this sense it also behaves like a 1st order RC filter. From the previous calculation the effective time constant t must be less than 10us/13.5 
=> fc > 1/2pt = 214.2kHz

D)	The main determinant of the amplifier’s noise is the thermal noise of the switches. However, this will be filtered by the input caps. So the total rms noise = sqrt(KT/C) < 1uV => C = (KT)/(1uV)^2 = 4.05nF => C1 = C2 = 8.1nF